## Slide 1
Top-Level View of Computer Function and Interconnection
Yuemin Ding
Tecnun, University of Navarra
Fall, 2021

## Slide 2: Outline
Computer components
Instruction fetch and execute cycles
Interrupts
Interconnection

## Slide 3: Hardwired v.s. Software Systems
Everything that can be done in software can also be done in hardware!
Two different implementations to sense the colour of cards.

## Slide 4: What do we still need software?
Hardwired systems are inflexible. It only accepts data and produces results.
Instead, we use:
  General purpose hardware can do different tasks, given correct control signals.
  Instead of re-wiring, supply a new set of control signals to general purpose hardware.
Hardwired programming
Software programming

## Slide 5: Components: Top Level View
Notes: The Control Unit and the Arithmetic and Logic Unit (ALU) constitute the Central Processing Unit
Data and instructions need to get into the system and results out
  Input/output
Temporary storage of code and results is needed
  Main memory
An interconnection component is also needed
  System bus

## Slide 6: Outline
Computer components
Instruction fetch and execute cycles
Interrupts
Interconnection

## Slide 7: Instruction Fetch and Execute
The processing required for a single instruction is called an instruction cycle.
Instruction cycle include two steps:
  Fetch cycle
  Execute cycle

## Slide 8: Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and generated control signals to perform actions

## Slide 9: Execute Cycle
Processor <-> memory
  data transfer between CPU and main memory
Processor<->I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump, if … else …
Combination of the above

## Slide 10: Instruction Fetch, Decode and Execute
Instruction address calculation (iac): Determine the address of the next instruction to be executed.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 11: Instruction Fetch, Decode and Execute
Instruction fetch (if): Read instruction from its memory location into the processor.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 12: Instruction Fetch, Decode and Execute
Instruction operation decoding (iod): Analyze instruction to determine type of operation to be performed and operand(s) to be used.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 13: Instruction Fetch, Decode and Execute
Operand address calculation (oac): If the operation involves reference to an operand in memory or available via I/O, then determine the address of the operand.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 14: Instruction Fetch, Decode and Execute
Operand fetch (of): Fetch the operand from memory or read it in from I/O.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 15: Instruction Fetch, Decode and Execute
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 16: Instruction Fetch, Decode and Execute
Operand fetch (of): Fetch the operand from memory or read it in from I/O.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 17: Instruction Fetch, Decode and Execute
Data operation (do): Perform the operation indicated in the instruction.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 18: Instruction Fetch, Decode and Execute
Operand address calculation (oac): If the operation involves reference to an operand in memory or available via I/O, then determine the address of the operand.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 19: Instruction Fetch, Decode and Execute
Operand store (os): Write the result into memory or out to I/O.
Fetch Decode Execute
Example: Add A,B iac, if, iod, oac, of, oac, of, do, oac, os

## Slide 20: Outline
Computer components
Instruction fetch and execute cycles
Interrupts
Interconnection

## Slide 21: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing

## Slide 22: Interrupt Cycle
Interrupt cycle is added to instruction cycle
Without interrupt
With interrupt

## Slide 23: Interrupt types
Types of Interrupts:
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error

## Slide 24: Program Timing - Short I/O Wait

## Slide 25: Program Timing - Long I/O Wait

## Slide 26: Instruction Cycle (with Interrupts) - State Diagram

## Slide 27: Multiple Interrupts-Solutions
Disable Multiple interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur

## Slide 28: Multiple Interrupts-Solutions
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt

## Slide 29: Time Sequence of Multiple Interrupts

## Slide 30: Outline
Computer components
Instruction fetch and execute cycles
Interrupts
Interconnection

## Slide 31: Interconnection Structures
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU

## Slide 32: Memory <-> Processor
Processor  Memory
Control signals (e.g. Read/Write)
Address
Data
Memory  Processor
Instructions
Data

## Slide 33: I/O <-> Processor
Processor  I/O
Control signals (e.g. Read/Write)
Address
Internal Data (e.g. stored file for printing)
I/O  Processor
Interrupt signals
Internal Data (e.g. keyboard signal)
I/O external signal
Input: mouse click
Output: monitor display

## Slide 34: I/O <-> Memory
To improve performance of processor, I/O is allowed to exchange data directly with memory
This is realized with a secondary chip and the data exchange is not necessary to go through the processor.
I/O controler

## Slide 35: Interconnection structures
In computer system, the most common interconnection structures are:
The bus and multi-bus structure
Point-to-point interconnection

## Slide 36: What is a Bus?
A communication pathway connecting two or more devices
A signal transmitted by any one device is available for reception by all other devices.
If two devices transmit during the same time period, their signals will overlap and become garbled.
Lines may be grouped for data transmission, e.g. 8, 16, 32, 64.

## Slide 37: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit
…
A word in memory
Data bus Width

## Slide 38: Address bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space
216 = 64k
0x0000
0x0001
0xFFFF
…
…

## Slide 39: Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals

## Slide 40: Buses in computer
What do buses look like?
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
  Sets of wires

## Slide 41: Question 1
How does a CPU write a word into the memory cell with the bus system?

## Slide 42: Question 2
How does an I/O inform the CPU that the data is ready with the bus system?

## Slide 43: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
    Long data paths mean that coordination of bus use can adversely affect performance
    Aggregated data transfer approaches bus capacity
Most systems use multiple buses to overcome these problems

## Slide 44: Multiple Buses
44

## Slide 45: Point-to-Point Interconnect
The conventional bus encountered difficulties for higher and higher data rates due to electrical constraints.
Point-to-point connections (e.g. QPI and PCIe) can be established between each pair of cores and cores and I/O Hub.

## Slide 46: PCI Express
PCI Express is based on the Peripheral Component Interconnect (PCI), a high-bandwidth bus for high-speed I/O subsystems
PCIe has been developed as a point-to-point interconnection to keep pace with the high-rate demand of attached I/O device, such as Gigabit Ethernet.
QPI
Memory bus

## Slide 47: Interconnection of an Intel platform

## Slide 48: Thank you! Q&A